## Slide 1: Automotive Application of an Advanced Power Conversion for Brushless Motor Control Gerry Chen, Zhongxi Li, Carol Xia, Raj Borra, Sam Osheroff, Angel Peterchev, Stefan Goetz Duke University, Durham, USA
State of Art Electrical Vehicle and Problems
[1] Goetz, Stefan M., et al. "Control of Modular Multilevel Converter With Parallel Connectivity—Application to Battery Systems." IEEE Transctions on Power Electronics 32.11 (2017): 8381-8392.
[2] Z. Li, A. V. Peterchev, R. Lizana, and S. M. Goetz, “Distributed Balancing Control for Modular Multilevel Series/Parallel Converter with Capability of Sensor-less Operation,” in Energy Conversion Congress and Exposition (ECCE), 2017 IEEE, 2017.
References
Hard-wired batteries
Bad fault-tolerance
Needs complex battery management circuit
Controller
Output distortion
Large EMI
Motor
Large torque ripple
Large noise
Large insulation stress
Our Solution : Intelligent Battery Modules
Modular batteries [1]
Battery interfaced by switches
Smart control [2]
Sensor-less balancing
Minimal losses
Module Design
High-power circuit
LiPo batteries
Electrical & Thermal Testing
Future Work : Assembly
High-quality output
Less toque ripple
Less insulation stress
Great fault-tolerance
Intelligent battery module
Motor Control
Thickness (mm) | (W/mK) | (°C) | Cost / board | Digikey PN
0.127 | 1.8 | 0.24 | $4.28 | 1168-1384-ND‎
0.5 | 1.5 | 1.11 | $4.70 | ‎BER161-ND‎
1 | 1.0 | 3.33 | $2.67 | ‎3M156051-ND‎
2 | 1.5 | 4.44 | $8.05 | ‎BER164-ND‎
Thickness (mm) |  |  | Cost / board | Digikey PN
0.127 | 1.8 | 0.24 | $4.28 | 1168-1384-ND‎
0.5 | 1.5 | 1.11 | $4.70 | ‎BER161-ND‎
1 | 1.0 | 3.33 | $2.67 | ‎3M156051-ND‎
2 | 1.5 | 4.44 | $8.05 | ‎BER164-ND‎
Thermal Pad Comparison
MOSFET selection:
Frequency and dead-time: ~4kHz optimal
Losses dominated by RDS
Thermal capacity of copper sufficiently large
Field-Oriented Control takes full advantage of precise current control ability
Stable operation for setpoint and sensed speed changes